## Slide 1: perfSONAR on Low Cost Hardware
Antoine Delvaux (adelvaux@man.poznan.pl)
Szymon Trocha (szymon.trocha@man.poznan.pl)
Trupti Kulkarni (GEANT), Ivan Garnizov (DFN/Univ Erlangen)
TNC16, Prague
13/06/2016

## Slide 2: Agenda
Small Nodes? Yes!
Examples, limitations and usefulness
Small Nodes in GÉANT
  Hardware
  Setup
Questions & Answers

## Slide 3: Footprint increase

## Slide 4: Small Nodes?
Many different experimentations
  cheap deployments and small form factor
  more deployments, more useful perfSONAR is
Early trials
  Very cheap HW: Cubox, Beaglebone, Raspberry Pi, …
  ARM based challenge (no CentOS support)
Survey
33%

## Slide 5: Small Nodes!
Survey results: Inexpensive but with known capabilities:
  1 Gbps with enough RAM and disk space
perfSONAR project official support from 3.5 onwards
  Debian support (easier for ARM devices)
  Improved central management
Cost target: € 200
  Many different hardware choices

## Slide 6: Examples
Intel NUC kit
ASUS Chromeux
Liva I/X/X2
Gigabyte BRIX
Zotac BOX
Servers Direct/Supermicro

## Slide 7: Limitations: what to look at
CPU power, RAM (8 GB preferred)
Multiple NIC?
Disk space (or use central server)
Form factor (rack mount, durability, …)
Newer, better, always coming soon!
You get what you pay for… tradeoffs always.

## Slide 8: So this replaces large server?
No, not really.
More memory, higher speed, warranties, stability
Useful for custom and numerous deployments or as starters’ boxes
IoT?
Notes: Still need to have larger boxes with more memory, higher speed, warranties, stability.
Useful for custom and numerous deployments or as starters’ boxes.

## Slide 9: Small Node in GÉANT
Enable you to have first hand experience with perfSONAR
  Easy and useful setup
6 months project with
  provided hardware
  central server and support run by GÉANT SA2T3
Launch: TNC2016
Notes: GÉANT run central server
GÉANT perfSONAR experts to provide support

## Slide 10: Measurements
to 8 GÉANT MPs
  geographically spread
  throughput (4)
  latency/loss (4)
  IPv4 and IPv6
Optionally between small nodes
Central server: GÉANT
Add your own measurements, experiment yourself

## Slide 11: Hardware chosen
GIGABYTE BRIX
  GB-BACE-3150
1 x SO DIMM DDR3L 1.35 — 8GB RAM
1Gb/s RJ45 LAN Realtek
WiFi + BT
VGA, HDMI
4 x USB 3.0
Micro SD
External power supply
6 x 11 x 11 cm
Durable chassis

## Slide 12
What’s inside? Current configuration
Intel Celeron N3150 1.6GHz
4 cores
8GB RAM Kingston
120GB
Patriot SSD
/ 20 GB
/var/lib 86 GB
Swap 8 GB

## Slide 13: Other initial settings
pre-install of the perfSONAR toolkit 3.5.1
  CentOS 6
Administrative accounts: psudouser, pswebadmin, geantadmin
root remote login disabled
Auto-updates enabled by default
Tagged with communities : GEANT, pSmall-GEANT
Initial networking with DHCP
Monitoring with SNMP (deamon runnig)
1 master node, rest cloned

## Slide 14: Initial performance
Selftest efficiency
NTP observations

## Slide 15: Known limitations
No heating problems observed
Some mitigations made but need more feedback from you
Single NIC
Competing BW + OWD
Limited queuing
Resources
CPU limits
HDD storage
Using the same interface
NTP

## Slide 16: Setting up your pSmall node
Power on and access locally or via SSH
Connect to the network and configure IPv4 and IPv6
Launch Web interface and configure basic settings to describe the node
Modify NTP
Inform GÉANT perfSONAR support team
perfsonar-smallnodes@lists.geant.org

## Slide 17: Recommendations and usage
Deploy it in the core of your network
Assign fixed IPv4 and IPv6 address and don’t change it later
Define stable DNS name
Add your own measurements through the webUI
  other European NREN and Organisations
  the R & E networks worldwide
  other Small Nodes
Free to experiment with the node
Use ServicesDirectory

## Slide 18: How to get support?
From the Small Nodes project during 6 months
  project mailing list
  central server operations
  help in running the small node
From other perfSONAR resources
  Users mailing list (perfsonar-user@internet2.edu)
  Global website (http://www.perfsonar.net/)

## Slide 19: What’s next?
Visit dashboard to check performance
  http://perfsonar-smallnodes.geant.org/maddash-webui/
Participate to the mailing list
  perfsonar-smallnodes@lists.geant.org
  https://lists.geant.org/sympa/info/perfsonar-smallnodes
Report at STF / High Performance Networking workshop in July in Vienna
  https://eventr.geant.org/events/2428
Evaluation in 4 to 6 months

## Slide 20: Requirements to participate
Belonging to the R & E community
  Being part of a networking team, service or research group
  Identified responsible person to sign agreement
Priority given to GÉANT Service Area organisations and/or small organisations
Note: Node remains property of GÉANT

## Slide 21: TNC2016: perfSONAR on Low Cost HardWare
TNC 2016
13rd of June 2016
Antoine Delvaux — PSNC/GÉANT adelvaux@man.poznan.pl
Szymon Trocha — PSNC/GÉANT szymon.trocha@man.poznan.pl